## Slide 1: Chapter 2
Instructions: Language of the Computer

## Slide 2: ISA: A Thin Software/Hardware Interface
Instruction Set Architecture
I/O System
Processor
Digital Design
Circuit Design
Datapath & Control
Transistors
Memory
Hardware
Compiler
Operating
System
Application
Software
Assembler
ISA as an abstraction
  A model for machine-level programming
  Abstracts the underlying implementation/technology

## Slide 3: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common

## Slide 4: Instruction Set Architectures
Early computers had very simple instruction sets
  Simplified implementation
Later trend was to add more and more instructions to new CPUs to do elaborate operations
  VAX architecture had an instruction to multiply polynomials!
RISC philosophy (Cocke IBM, Patterson, Hennessy, 1980s) – Reduced Instruction Set Computing
  Keep the instruction set small and simple, makes it easier to build fast hardware.
  Let software do complicated operations by composing simpler ones.

## Slide 5: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B & E
Why MIPS instead of Intel x86?
  MIPS is simple, elegant. Don’t want to get bogged down in gritty details.
  MIPS widely used in embedded apps, x86 little used in embedded, and more embedded computers than PCs

## Slide 6: MIPS (RISC) Design Principles
Simplicity favors regularity
  Fixed size instructions: 32 bits
  Small number of instruction formats
  Opcode always the first 6 bits
Smaller is faster
  Small instruction set
  Limited number of registers
  Few addressing modes
Make the common case fast
  Arithmetic/logic operands in registers
  Immediate operands (16 bits)
Good design demands good compromises
  Three instruction formats
  Fields are aligned as much as possible

## Slide 7: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost

## Slide 8: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 9: Simplicity and Regularity
In MIPS ISA:
  All Instructions have the same length: 32 bits
  Limited number of instruction formats: 3
  Instruction fields (opcode, operands) are aligned among the different formats
  Arithmetic/logic instructions have 3 operands
    Each operand is 32 bits wide
By comparison, in x86 ISA:
  Instruction length varies from 1 to 17 bytes
  Many instruction formats
  Only two operands
    One of the operands serves also as destination

## Slide 10: Assembly Variables: Registers
Unlike HLL like C or Java, assembly cannot use variables
  Why not? Keep Hardware Simple
Assembly Operands are registers
  Limited number of special locations built directly into the hardware
  Operations can only be performed on these!
Benefit: Since registers are directly in hardware, they are very fast (faster than 1 ns - light travels 30cm in 1 ns!!! )

## Slide 11: Registers
Register: a small container of data in the CPU
  Not part of memory
  Has very fast access (much faster than memory)
  Capacity (width) is small: fixed number of bits
MIPS has 32 general purpose registers
  Why 32? Smaller is faster, but too small is bad. Goldilocks problem.
  Drawback: Since registers are in hardware, there are a predetermined number of them.
  Solution: MIPS code must be very carefully put together to efficiently use registers
  Registers are numbered 0 to 31
  Each register has width 32 bits (called a “word”)
  Many instructions use only register operands (speed!)
Registers are divided into groups
  Each group has a specific role (or usage) by convention
  Registers have symbolic names that reflect their role
  Roles are exploited by compilers to allocate data to registers

## Slide 12: Names of MIPS Registers
Each register can be referred to by number or name
Number references:
  $0, $1, $2, … $30, $31
But also
  $16 - $23 $s0 - $s7 (correspond to C variables)
  $8 - $15  $t0 - $t7 (correspond to temporary variables)
  More registers to come…
In general, use names to make your code more readable

## Slide 13: MIPS General Purpose Registers

## Slide 14: C, Java variables vs. registers
In C (and most High Level Languages) variables declared first and given a type
  Example: int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix and match int and char variables).
In Assembly Language, registers have no type; operation determines how register contents are treated

## Slide 15: Using Data in Registers
Arithmetic/logic operations work only on registers (never on values in memory)
  One of the operands must be a register
  The other operand can be a register or a constant
  The result is always placed in register
There are “only” 32 registers
  What if there is more data than free registers?
  Some registers can be spilled (copied) to memory

## Slide 16: MIPS Register File
Holds 32 registers, each 32-bits wide
  Two read ports and one write port
Designed for fast 3-operand arithmetic on registers
  reg3 = reg1 op reg2
Reads two registers and writes one register in a single cycle
  Read data is available during entire cycle
  Write is clocked at the end of the cycle
   One register can be both read and then written in same cycle
Clock
5
5
5
32
32
32

## Slide 17: Big Idea: Stored-Program Computer
  Instructions are represented as bit patterns - can think of these as numbers.
  Therefore, entire programs can be stored in memory to be read or written just like data.
  Can reprogram quickly (seconds), don’t have to rewire computer (days)
  Known as the “von Neumann” computers after widely distributed tech report on EDVAC project
First Draft of a Report on the EDVAC
by
John von Neumann
Contract No. W–670–ORD–4926
Between the
United States Army Ordnance Department and the
University of Pennsylvania
Moore School of Electrical Engineering
University of Pennsylvania
June 30, 1945

## Slide 18: Consequence #1: Everything Addressed
Since all instructions and data are stored in memory, everything has a memory address: instructions, data words
  both branches and jumps use these
C pointers are just memory addresses: they can point to anything in memory
  Unconstrained use of addresses can lead to nasty bugs; up to you in C; limited in Java by language design
One register keeps address of instruction being executed: “Program Counter” (PC)
  Basically a pointer to memory: Intel calls it Instruction Pointer (a better name)

## Slide 19: Consequence #2: Binary Compatibility
Programs are distributed in binary form
  Programs bound to specific instruction set
  Different version for Macintoshes and PCs
New machines want to run old programs (“binaries”) as well as programs compiled to new instructions
Leads to “backward-compatible” instruction set evolving over time
Selection of Intel 8086 in 1981 for 1st IBM PC is major reason latest PCs still use 80x86 instruction set (Pentium 4); could still run program from 1981 PC today

## Slide 20: Von Neumann architecture scheme

## Slide 21: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations

## Slide 22: Addition and Subtraction of Integers
Addition in Assembly
  Example: add $s0,$s1,$s2 (in MIPS)
  Equivalent to: a = b + c (in C)
  where C variables ⇔ MIPS registers are:
  a ⇔ $s0, b ⇔ $s1, c ⇔ $s2
Subtraction in Assembly
  Example: sub $s3,$s4,$s5 (in MIPS)
  Equivalent to: d = e - f (in C)
  where C variables ⇔ MIPS registers are: d ⇔ $s3, e ⇔ $s4, f ⇔ $s5

## Slide 23: Addition and Subtraction of Integers Example 1
How to do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add $t0, $s1, $s2 # temp = b + c
  add $t0, $t0, $s3 # temp = temp + d
  sub $s0, $t0, $s4 # a = temp - e
A single line of C may break up into several lines of MIPS.
Notice the use of temporary registers – don’t want to modify the variable registers $s
Everything after the hash mark on each line is ignored (comments)

## Slide 24: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory

## Slide 25: Main Memory
Linear array of memory cells
  Each cell has its own address
    Cell address is similar to array index
In MIPS, each cell is one byte wide (8 bits)
  Byte is the smallest size accessible in memory
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 26: Memory Addresses
0
1
2
3
…
A “word” is 4 consecutive bytes starting at an address that is a multiple of 4 (word-aligned)
  The address of a word points to the byte with lowest address
Maximum memory size in MIPS
  232 bytes = 4GBytes = 230 words
Memory addresses are really in bytes, not words
0
4
8
12
…
1
5
9
13
…
2
6
10
14
…
3
7
11
15
…
Addr of lowest byte in word is addr of word

## Slide 27: Order of Bytes in a Word Value
A word-size value in memory can be kept in two ways
  Little Endian: lowest address contains least significant byte
  Big Endian: lowest address contains most significant byte
For example: integer value 0x46788756 stored at address 1000 in memory
MIPS implementation can be Little or Big Endian
      MARS Simulator uses Little Endian
Address
Content
Address
Content

## Slide 28: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 29: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
Offset must be a constant known at assembly time.
$s3 – base register (pointer)
32, 48 – offsets in bytes
$s3+32 and $s3+48 must be multiples of 4
offset
base register

## Slide 30: Loading and Storing bytes
In addition to word data transfers (lw, sw), MIPS has byte data transfers:
  load byte: lb
  store byte: sb
Same format as lw, sw
E.g., lb $s0, 3($s1)
  contents of memory location with address = sum of “3” + contents of register $s1 is copied to the low byte position of register $s0.
byte loaded
zzz zzzz
x
…is copied to “sign-extend”
This bit
xxxx xxxx xxxx xxxx xxxx xxxx
$s0:

## Slide 31: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 32: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 33: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero

## Slide 34: Overflow in Arithmetic
Reminder: Overflow occurs when there is a “mistake” in arithmetic due to the limited precision in computers.
Example (4-bit unsigned numbers):
  15 1111
  + 3 + 0011
  18 10010
But we don’t have room for 5-bit solution, so the solution would be 0010, which is +2, and “wrong”.

## Slide 35: Overflow handling in MIPS
Some languages detect overflow (Ada), some don’t (most C implementations)
MIPS solution is 2 kinds of arithmetic instructions:
  These cause overflow to be detected
    add (add)
    add immediate (addi)
    subtract (sub)
  These do not cause overflow detection
    add unsigned (addu)
    add immediate unsigned (addiu)
    subtract unsigned (subu)
Compiler selects appropriate arithmetic
  MIPS C compilers produce addu, addiu, subu

## Slide 36: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23

## Slide 37: Instructions as Numbers (1/2)
How do we represent instructions?
  Remember: Computer only understands 1s and 0s, so “add $t0,$0,$0” is meaningless.
  MIPS/RISC seeks simplicity: since data is in words, make instructions be fixed-size 32-bit words also.

## Slide 38: Instructions as Numbers (2/2)
One word is 32 bits, so divide instruction word into “fields”.
Each field tells processor something about instruction.
We could define different fields for each instruction, but MIPS seeks simplicity, so define 3 basic types of instruction formats:
  R-format
  I-format
  J-format

## Slide 39: MIPS Instruction Formats
op – opcode rs – 1st source register
funct – function-code rt – 2nd source register / target register
shamt – shift amount rd – destination register
immediate – 16-bit constant/offset
address – 26-bit “pseudo-direct” address
Design Principle 4: Good design demands good compromises
      Different formats complicate decoding, but allow 32-bit instructions uniformly
      Keep formats as similar as possible
Formats are aligned as much as possible
  Common field positions and semantics

## Slide 40: R-Format Instructions (1/5)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 5 + 5 + 6 = 32
For simplicity, each field has a name:
Important: On these slides and in book, each field is viewed as a 5- or 6-bit unsigned integer, not as part of a 32-bit integer.
  Consequence: 5-bit fields can represent any number 0-31, while 6-bit fields can represent any number 0-63.
6
5
5
5
6
5
opcode
rs
rt
rd
funct
shamt

## Slide 41: R-Format Instructions (2/5)
What do these field integer values tell us?
  opcode: partially specifies what instruction it is
    Note: This number is equal to 0 for all R-Format instructions.
  funct: combined with opcode, this number exactly specifies the instruction
Question: Why aren’t opcode and funct a single 12-bit field?
  We’ll answer this later.

## Slide 42: R-Format Instructions (3/5)
More fields:
  rs (Source Register): usually used to specify register containing first operand
  rt (Target Register): usually used to specify register containing second operand (note that name is misleading)
  rd (Destination Register): usually used to specify register which will receive result of computation

## Slide 43: R-Format Instructions (4/5)
Notes about register fields:
  Each register field is exactly 5 bits, which means that it can specify any unsigned integer in the range 0-31. Each of these fields specifies one of the 32 registers by number.
  The word “usually” was used because there are exceptions that we’ll see later. E.g.,
    mult and div have nothing important in the rd field since the dest registers are hi and lo
    mfhi and mflo have nothing important in the rs and rt fields since the source is determined by the instruction (see COD)

## Slide 44: R-Format Instructions (5/5)
Final field:
  shamt: This field contains the amount a shift instruction will shift by. Shifting a 32-bit word by more than 31 is useless, so this field is only 5 bits (so it can represent the numbers 0-31).
  This field is set to 0 in all but the shift instructions.
For a detailed description of field usage for each instruction, see green insert in COD

## Slide 45: R-Format Example (1/2)
MIPS Instruction:
  add $8,$9,$10
  opcode = 0 (look up in table in book)
  funct = 32 (look up in table in book)
  rd = 8 (destination)
  rs = 9 (first operand)
  rt = 10 (second operand)
  shamt = 0 (not a shift)

## Slide 46: R-Format Example (2/2)
MIPS Instruction:
  add $8,$9,$10
  Decimal number per field representation:
  Binary number per field representation:
  hex representation: 012A 4020hex
  decimal representation: 19,546,144ten
  Called a Machine Language Instruction
0
9
10
8
32
0
000000
01001
01010
01000
100000
00000
hex

## Slide 47: MIPS Op-codes and Funct-codes
See “Green Sheet” in the textbook

## Slide 48: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 49: Shift Instructions
shamt: how many positions to shift
rs: not used (always 0)
Shift left logical (sll)
  Shift to the left. fill zero bits on the right
  sll rd,rt,i # rt shifted left i positions
  Shift i positions effectively multiplies by 2i
Shift right logical (srl)
  Shift to the right, fill zero bits on the left
  srl rd,rt,i # rt shifted right i positions
  Shift i positions effectively divides by 2i (unsigned only)
Shift right arithmetic (sra)
  Shift to the right, replicate sign bit on the left
  sra rd,rt,i # rt shifted right arithm. i positions
  Shift i positions effectively divides by 2i
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 50: Logic Shifting
Shift Left: sll $s1,$s2,2 #s1=s2<<2
  Store in $s1 the value from $s2 shifted 2 bits to the left (they fall off end), inserting 0’s on right; << in C.
    Before: 0000 0002hex 0000 0000 0000 0000 0000 0000 0000 0010two
  After: 0000 0008hex 0000 0000 0000 0000 0000 0000 0000 1000two
  What arithmetic effect does shift left have?
Shift Right: srl is opposite shift; >>

## Slide 51: Arithmetic Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
1111 1111 1111 1111 1111 1111 1111 1110two= -2ten
  Unfortunately, this is NOT same as dividing by 2n
    Fails for odd negative numbers
    C arithmetic semantics is that division should round towards 0
Notes: \

## Slide 52: I-Format Instructions (1/4)
What about instructions with immediates?
  5-bit field only represents numbers up to the value 31: immediates may be much larger than this
  Ideally, MIPS would have only one instruction format (for simplicity): unfortunately, we need to compromise
Define new instruction format that is partially consistent with R-format:
  First notice that, if instruction has immediate, then it uses at most 2 registers.

## Slide 53: I-Format Instructions (2/4)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 16 = 32 bits
  Again, each field has a name:
  Key Concept: Only one field is inconsistent with R-format. Most importantly, opcode is still in same location.
6
5
5
16
opcode
rs
rt
immediate

## Slide 54: I-Format Instructions (3/4)
What do these fields mean?
  opcode: same as before except that, since there’s no funct field, opcode uniquely specifies an instruction in I-format
  This also answers question of why R-format has two 6-bit fields to identify instruction instead of a single 12-bit field: in order to be consistent as possible with other formats while leaving as much space as possible for immediate field.
  rs: specifies a register operand (if there is one)
  rt: specifies register which will receive result of computation (this is why it’s called the target register “rt”) or other operand for some instructions.

## Slide 55: I-Format Instructions (4/4)
The Immediate Field:
  addi the immediate is sign-extended to 32 bits. Thus, it’s treated as a signed integer.
  16 bits  can be used to represent immediate up to 216 different values
  This is large enough to handle the offset in a typical lw or sw.
  Later, we’ll see what to do when a value is too big for 16 bits
lw $t0, 32($s3)
sw $t0, 48($s3)

## Slide 56: I-Format Example (1/2)
MIPS Instruction:
  addi $21,$22,-50
  opcode = 8 (look up in table in book)
  rs = 22 (register containing operand)
  rt = 21 (target register)
  immediate = -50 (by default, this is decimal in assembly code)

## Slide 57: I-Format Example (2/2)
MIPS Instruction:
  addi $21,$22,-50
8
22
21
-50
001000
10110
10101
1111111111001110
  Decimal/field representation:
  Binary/field representation:
  hexadecimal representation: 22D5 FFCEhex
  decimal representation: 584,449,998ten

## Slide 58: Logical Operations
Make bitwise changes
Useful for handling selected bits/fields
  extract, insert, mask, flip
Logical instructions have format R or I
  In format I, the immediate value is always unsigned
Operation | C/C++ | Java | MIPS
Shift left | << | << | sll
Shift right logical | >> (for unsigned type) | >>> | srl
Shift right arithmetic | >> (for signed type) | >> | sra
Bitwise AND | & | & | and,andi
Bitwise OR | ¦ | ¦ | or,ori
Bitwise NOR | n/a | n/a | nor
Bitwise XOR | ^ | ^ | xor,xori
Bitwise NOT | ~ | ~ | (uses nor)

## Slide 59: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word

## Slide 60: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 61: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 62: Bitwise NOT
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS does not have a NOT opcode
  Use NOR instead
  rd=NOT(rs) is equivalent to rd=NOR(rs,$0)
nor rd,rs,$0
0001 0000 0000 0000 0011 1100 0000 0010
rs
0000 0000 0000 0000 0000 0000 0000 0000
$0
1110 1111 1111 1111 1100 0011 1111 1101
nor(rs,$0)