## Slide 1: Chapter 2
Instructions: Language of the Computer

## Slide 2: Types of Branches
Branch – change of control flow
Conditional Branch – change control flow depending on outcome of comparison
  branch if equal (beq) or branch if not equal (bne)
Unconditional Branch – always branch
  a MIPS instruction for this: jump (j)

## Slide 3: Types of Branches
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1

## Slide 4: Instruction Labels
An instruction in a source program can have a label
  It is a symbolic name for the memory address where the instruction resides
    The assembler will calculate the numeric address
  Each label in the program must be unique
  Labels can be used as operands in some instructions
    Typically as targets in branch/jump instructions

## Slide 5: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …
Assembler calculates addresses

## Slide 6: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 7: Coding “if-then-else” in MIPS
C code:
if (i==j) f=g+h; else f=g-h;
MIPS code:
   f,g,h,i,j are in $s0,$s1,$s2,$s3,$s4
bne $s3,$s4,else # if i!=j goto else add $s0,$s1,$s2 # f=g+h j endif # goto endif else: sub $s0,$s1,$s2 # f=g-h endif: …
reverse the condition logic

## Slide 8: Coding a “while” Loop in MIPS
C code:
while (A[i]!=k) i+=1;
MIPS code:
  i is in $s3, k in $s5, base address of A in $s6
loop: sll $t1,$s3,2 # $t1=i*4 add $t1,$t1,$s6 # $t1=$t1+&A lw $t0,($t1) # $t0=memory[$t1] beq $t0,$s5,endl # if done goto endl addi $s3,$s3,1 # i+=1 j loop # goto loop endl: …
reverse the condition logic

## Slide 9: Branching Instruction Usage
Conditional branches typically used for
if-else, while, for control structures.
  These structures are usually small (< 50 instructions)
  Function calls and unconditional jumps handled with jump instructions (J-Format)
Recall: Instructions stored in a localized area of memory (Code/Text)
  Address of current instruction stored in the program counter (PC)

## Slide 10: Encoding of Conditional Branch Instruction : PC-Relative Addressing
Conditional branch instructions have format I
Recall: MIPS uses 32-bit addresses
  Memory is byte-addressed
  Instructions are word-aligned
  Address is always multiple of 4 (in bytes), meaning it ends with 0b00 in binary
  Number of bytes to add to the PC will always be a multiple of 4
op
rs
rt
offset from PC
6 bits
5 bits
5 bits
16 bits

## Slide 11: Encoding of Conditional Branch Instruction : PC-Relative Addressing
  wordOffset denotes the distance from the instruction pointed by PC to the target Instruction
  wordOffset is in units of words (not bytes)
  Can now branch ± 215 words
  We can reach 216 instructions = 218 bytes around PC.
op
rs
rt
wordOffset from PC
6 bits
5 bits
5 bits
16 bits

## Slide 12: Program Execution Model
To run a program, it has to be loaded in main memory
  Code (machine instructions)
  Data
The CPU has a register called PC (Program Counter)
  Contains the address of the next instruction to be executed
  PC is not one of the 32 general purpose registers
Instruction Execution Cycle Performed by the CPU logic
  Get the next instruction from memory
    Address of instruction is in the PC
  Advance the PC to the next instruction
    PC=PC+4 (instructions are word-aligned)
  Execute the instruction
  Go back to Step 1
Why PC is modified before instruction is executed ? Hardware reasons; will be clear why later in the course.

## Slide 13: Branch Calculation
wordOffset is relevant in step 3 of the execution cycle
  Observe that PC was already changed in step 2
Example :
  this: beq rs,rt,next
  In step 2 of the execution cycle: PC = this + 4
  Therefore, in step 3:
  next = PC + wordOffset*4 = this + 4 + wordOffset*4
  wordOffset = (next – this - 4)/4
wordOffset is calculated by the assembler.

## Slide 14: Branch Example (1/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
I-Format fields:
  opcode = 4 (look up on Green Sheet)
  rs = 9 (first operand)
  rt = 0 (second operand)
  immediate = ???
Start counting from instruction AFTER the branch
1
2
3
3

## Slide 15: Branch Example (2/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
  Field representation (decimal):
  Field representation (binary):
4
9
0
3
31
0
000100
01001
00000
0000000000000011
31
0

## Slide 16: PC-Relative addressing
If we don’t take the branch:
  PC = PC + 4 = next instruction
If we do take the branch:
  PC = (PC + 4) + (immediate*4)
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no
Notes: As we will see, jumping instructions can reach farther than branching

## Slide 17: Conditional Branch Design
MIPS has only “branch if equal” or “not equal”
Why not blt (branch if less than), bge (greater or equal), etc.?
  Hardware for <, ≥, … is slower than =, ≠
  Entails more work per instruction
     Requires a slower clock
    All instructions are penalized by slower clock!
beq and bne are the common case
This is a good design compromise
So, how can we use other conditional branches?

## Slide 18: More Conditional Operations
Set register to 1 if less than
slt rd,rs,rt
  if (rs < rt) then rd = 1; else rd = 0;
slti rt,rs,immediate
  if (rs < immediate) then rt = 1; else rt = 0;
This can be used in combination with beq, bne to form any conditional branch (<,<=,>,>=)
Example: coding of “branch if less or equal”
if ($s1 ≤ $s2) branch to label
  slt $at,$s2,$s1 #if ($s2<$s1) $at=1; else $at=0
  beq $at,$0,label #if $at=0 goto label
interim register

## Slide 19: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 20: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 21: Dealing With Large Immediates (1/2)
How do we deal with 32-bit immediates?
  Sometimes want to use immediates > ± 215 with addi, lw, sw and slti
  Bitwise logic operations with 32-bit immediates
Solution: Don’t mess with instruction formats, just add a new instruction
Load Upper Immediate (lui)
  lui reg,imm
  Moves 16-bit imm into upper half (bits 16-31) of reg and zeros the lower half (bits 0-15)

## Slide 22: Dealing With Large Immediates (2/2)
How can we load a 32-bit constant into a register?
101010101010101011001100110011002 = aaaacccc16
  Split it in two halves, and use 2 “immediate” instructions
  First, insert the upper half using “load upper immediate”
lui $at,0xaaaa
  Then, insert the lower half using “or immediate”
ori $t0,$at,0xcccc
This is available as the “load immediate” pseudo-instruction
  li $t0,0xaaaacccc
1010101010101010
0000000000000000
1100110011001100
0000000000000000
1010101010101010
1100110011001100
1010101010101010
0000000000000000
$at
$at
$t0
Bitwise OR
immediate
all zeros

## Slide 23: Assembler Pseudo-Instructions
Most assembler instructions represent machine instructions one-to-one.
Certain C statements are implemented unintuitively in MIPS
  e.g. assignment (a=b) via add zero
MIPS has a set of “pseudo-instructions” to make programming easier
  More intuitive to read, but get translated into actual instructions later
Example:
move dst,src translated into addi dst,src,0
blt $t0, $t1, L translated into
slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary

## Slide 24: Assembler Pseudo-Instructions
MARS has additional pseudo-instructions - See Help (F1) for full list

## Slide 25: Assembler Register
Problem:
  When breaking up a pseudo-instruction, the assembler may need to use an extra register
  If it uses a regular register, it’ll overwrite whatever the program has put into it
Solution:
  Reserve a register ($1 or $at for “assembler temporary”) that assembler will use to break up pseudo-instructions
  Since the assembler may use this at any time, it’s not safe to code with it

## Slide 26: Pseudo-Instructions for Data Access via Labels
The address (location) of a label is a 32-bit constant
  A label can be used as pointer to data
  Assume labels y and list are declared in the data segment
.data 0x100104a0
y: .word 100
list: .word 0:10
Load/store word at label
lw/sw $s4,y
  Pseudo-instruction is implemented by:
lui $at,0x1001
lw/sw $s4,0x04a0($at)
Load address of label
la $s5,y
  Same as “load immediate” of a 32-bit constant (shown previously)
Load/store word in an array at label
lw/sw $t1,list($t2)
  Register $t2 is an offset (“quasi-index”) into the array
  Pseudo-instruction is Implemented by:
lui $at,0x1001
addu $at,$at,$t2
lw/sw $t1,0x04a4($at)

## Slide 27: MAL vs. TAL
True Assembly Language (TAL)
  The instructions a computer understands and executes
MIPS Assembly Language (MAL)
  Instructions the assembly programmer can use (includes pseudo-instructions)
  Each MAL instruction becomes 1 or more TAL instruction
TAL ⊂ MAL

## Slide 28: J-Format Instructions (1/5)
For branches, we assumed that we won’t want to branch too far, so we can specify a change in the PC
For general jumps (j and jal), we may jump to anywhere in memory
  Ideally, we would specify a 32-bit memory address to jump to
  Unfortunately, we can’t fit both a 6-bit opcode and a 32-bit address into a single 32-bit word

## Slide 29: J-Format Instructions (2/5)
Define two “fields” of these bit widths:
As usual, each field has a name:
Key Concepts:
  Keep opcode field identical to R-Format and I-Format for consistency
  Collapse all other fields to make room for large target address
6
26
31
0
opcode
target address
31
0

## Slide 30: J-Format Instructions (3/5)
We can specify 226 addresses
  Still going to word-aligned instructions, so add 0b00 as last two bits (multiply by 4)
  This brings us to 28 bits of a 32-bit address
Take the 4 highest order bits from the PC
  Cannot reach everywhere, but adequate almost all of the time, since programs aren’t that long
  Only problematic if code straddles a 256MB boundary

## Slide 31: J-Format Instructions (4/5)
Conditional Branch to a Far Target
  When a program is very large, the target of a conditional branch might be too far away
    Farther than +/- 215 instructions away
    Offset cannot be encoded using 16 bits
  Solution: rewrite the code
    Reverse the condition logic
    Use unconditional jump to the far instruction
  Example:
      ble $s0,$s1,Far
      bgt $s0,$s1,Near
      j Far Near: …

## Slide 32: J-Format Instructions (5/5)
Jump instruction:
  New PC = { (PC+4)[31..28], target address, 00 }
Notes:
  { , , } means concatenation { 4 bits , 26 bits , 2 bits } = 32 bit address
    Book uses || instead
  Array indexing: [31..28] means highest 4 bits
  For hardware reasons, use PC+4 instead of PC

## Slide 33: Questions on PC-addressing
What do we do if destination of a conditional branch is > 215 instructions away from branch?
  Other instructions save us
  beq $s0,$0,far bne $s0,$0,next # next instr  j far next: # next instr
Notes: As we will see, jumping instructions can reach farther than branching

## Slide 34: Unconditional Jump via Register
Unconditionally jump to the address contained in a register
jr rs
Instruction has format R
  Only the rs register is relevant
Main Use:
  When the full target address is computed by the program

## Slide 35: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 36: Instruction Encoding Example
  Assume Loop is at address 6553610 (=1000016)
  Notice the crossed order of registers in the binary code
    Except in branch instructions
Loop: add $t2, $t1, $s6 | 65536 | 0 | 9 | 22 | 10 | 0 | 32
sll $t1, $s3, 2 | 65540 | 0 | 0 | 19 | 9 | 2 | 0
lw $t0, -8($t1) | 65544 | 35 | 9 | 8 | -8 |  | 
bne $t0, $s5, End | 65548 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s4, 12 | 65552 | 8 | 20 | 19 | 12 |  | 
j Loop | 65556 | 2 | 16384 |  |  |  | 
End: … | 65560 |  |  |  |  |  | 
6 5 5 5 5 6
rd
rs
rt
(Loop&0x0FFFFFFF)>>2 = 65536/4 = 16384
(End ‒(PC+4))>>2 = (65560 ‒(65548+4))/4=2

## Slide 37: Instruction Encoding Example (Cont.)
  Binary and hexa representation of the encoding
000000 01001 10110 01010 00000 100000 | 01365020 | 0 | 9 | 22 | 10 | 0 | 32
000000 00000 10011 01001 00010 000000 | 00134880 | 0 | 0 | 19 | 9 | 2 | 0
100011 01001 01000 1111111111111000 | 8d28fff8 | 35 | 9 | 8 | -8 |  | 
000101 01000 10101 0000000000000010 | 15150002 | 5 | 8 | 21 | 2 |  | 
001000 10100 10011 0000000000001100 | 2293000c | 8 | 20 | 19 | 12 |  | 
000010 00000000000100000000000000 | 08004000 | 2 | 16384 |  |  |  | 
Binary by field Hexa Decimal by field
6 5 5 5 5 6
6 5 5 5 5 6
1638410 = 214= 400016

## Slide 38: Encoding of MIPS Instructions
op – opcode rs – 1st source register
funct – function-code rt – 2nd source register / target register
shamt – shift amount rd – destination register
immediate – 16-bit constant/offset
address – 26-bit “pseudo-direct” address
op rs rt rd shamt funct
op rs rt immediate
op address
R
I
J
6 5 5 5 5 6
Uniform 32-bit instruction length
Three different formats: R, I, J
Formats are aligned as much as possible
  Common field positions and semantics

## Slide 39: MIPS Addressing Modes

## Slide 40: Our First MIPS Program!